## Slide 1: Biodiesel production from sunflower oil by microwave-assisted transesterification
Authors: N.E. Magida, Prof. S. Marx and C. Schabort

## Slide 2: Outline
Background
Aim and objectives
Experimental
  Materials
  Method
  Analytical method
Results and discussion
Conclusion
Acknowledgements

## Slide 3: Background
Fossil fuels are being depleted
  Non-renewable resources
  Contribute to GHG emissions
Alternative fuel
  Biodiesel
Traditional biodiesel production process
  transesterification
Lee et al., 2008; Zabeti et al., 2009

## Slide 4: Background
Catalyst can be base (NaOH and KOH) or acid (H2SO4 and H3PO4)
Alcohols mostly used are ethanol and methanol
Triglycerides
Alcohol
3 Fatty acids
Glycerol
3
Banerjee and Chakraborty, 2009; Balat and Balat, 2010; Zhang et al., 2010

## Slide 5: Background
Traditional method
  60°C, 90minutes with heating jacket
Alternative heating system
  Microwave irradiation
Hypothesis:
  Transesterification under microwave
  high biodiesel yield
  short reaction
  short separation time
Azcan and Danisman, 2008; Vyas et al., 2010

## Slide 6: Aim and objectives
Microwave-assisted biodiesel production:
  Reagent loading (alcohol: oil ratio)
  Catalyst loading (wt% catalyst)
  Power use (irradiation intensity)
  Reaction time

## Slide 7: Experimental
Materials
Feedstock
  Sunflower oil
Alcohol
  Methanol
Catalyst
  KOH
Reactor and heating source
  Household microwave oven
Analyses
  GC, FTIR, viscometry

## Slide 8: Experimental
Microwave-assisted transesterification
Oil: Methanol ratio
  1:3, 1:6 and 1:9
Power use
  300W, 450W, 600W and 900W
Reaction time
  10, 20, 30, 40, 50 and 60 sec
KOH loading
  0.5 wt% and 1 wt%

## Slide 9: Analytical methods
Gas Chromatography (GC)
  FAME composition
Fourier Transformer-Infrared Spectroscopy (FTIR)
  Biodiesel yield
  Biodiesel properties
Viscometer tube
  Biodiesel yield

## Slide 10: Composition of sunflower oil
Name | Formula | Weight %
Palmitic acid | C16:0 | 8 (4-9)
Stearic acid | C18:0 | 1 (1-7)
Oleic acid | C18:1 | 20 (14-40)
Linoleic acid | C18:2 | 70 (48-74)

## Slide 11: Results and discussion
The produced fatty acid methyl ester (biodiesel) was analyzed using GC and had the similar composition to sunflower oil
A 100% purity was obtained at 1 wt% for all power settings

## Slide 12: Effect of power input
Chart: Reaction time (s)
| 10 | 20 | 30 | 40 | 50 | 60
300W | 0.75867 | 0.85 | 0.89081 | 0.96628 | 0.97417 | 0.95969
450W | 0.71813 | 0.88706 | 0.94875 | 0.96586 | 0.93054 | 0.92292
600W | 0.73 | 0.91542 | 0.9885 | 0.98311 | 0.94748 | 0.93
900W | 0.83 | 0.97069 | 0.95 | 0.91506 | 0.91 | 0.9

## Slide 13: Effect of Oil: Alcohol ratio
Chart: Reaction time (s)
| 10 | 20 | 30 | 40 | 50 | 60
'1:3 | 0.96 | 0.97 | 0.97 | 0.94 | 0.91 | 0.91
'1:6 | 0.88 | 0.93 | 0.96 | 0.98 | 0.89 | 0.86
'1:9 | 0.89 | 0.95 | 0.97 | 0.96 | 0.93 | 0.92

## Slide 14: Optimum yield of biodiesel (0.5 wt%)
Oil: methanol ratio | Power | Reaction time | Optimum yield
1:3 | 450W | 30 sec | 94%
1:6 | 600W | 30 sec | 98%
1:9 | 600W | 30 sec | 97%

## Slide 15: Effect of catalyst loading
Chart: Reaction time (s)
| 10 | 20 | 30 | 40 | 50 | 60
0.5 wt% | 0.88 | 0.89 | 0.94 | 0.92 | 0.87 | 0.86
1 wt% | 0.96 | 0.97 | 0.97 | 0.94 | 0.91 | 0.91
1.5 wt% | 0.88 | 0.89 | 0.95 | 0.79 | 0.74 | 0.72

## Slide 16: Energy consumption
The reaction time is approximately 2 hours and separation time approximately 24 hours with the traditional transesterification method
This is a high energy consumption method which use about 1.2 kWh to obtain a 95% conversion
With the microwave transesterification method, a 98% conversion was obtained with the energy input of only 0.08 kWh
This confirms that microwave transesterification reduce the energy consumption while producing higher yields of biodiesel
Leung et al., 2010

## Slide 17: Conclusion
Sunflower oil, methanol (3:1, 6:1 and 9:1) and KOH (0.5 wt% and 1wt%) were used to produce biodiesel
The reaction mixture was heated by microwave irradiation (300-900W and 10-60 sec)and the composition of methyl esters was determined using GC analysis
Biodiesel samples contained approximately 6 wt% C16:0, 1 wt% C18:0, 20 wt% C18:1 and 72 wt% C18:2 (98% purity)
A 98% biodiesel yield was obtained at 1:6 ratio (0.5 and 1 wt% KOH) at 600W and 450W (30 and 40 sec), respectively
The energy consumption was reduced by a factor of 15
from 1.2 kWh to 0.08 kWh

## Slide 18: Acknowledgements
Authors would like to acknowledge:
Coega Development Company for financial student support
National Research Foundation and SANERI/DST for financial research support
North West University

## Slide 19: References
Azcan, A. and Danisman, A. 2008. Microwave assisted transesterification of rapeseed oil. Fuel 87:1781-1788
Balat, M. and Balat, H. 2010. Progress in biodiesel processing. Applied Energy 87:1815–1835
Banerjee, A. and Chakraborty, R. 2009. Parametric sensitivity in transesteriﬁcation of waste cooking oil for biodiesel production—A review. Resources, Conservation and Recycling 53:490–497
Lee, S.K., Chou, H., Ham, T.S., Lee, T.S. and Keasling, J.D. 2008. Metabolic engineering of microorganisms for biofuels production: from bugs to synthetic biology to fuels. Current Opinion Biotechnology 19:556-563
Leung, D.Y.C., Wu, X. and Leung, M.K.H. 2010. A review on biodiesel production using catalyzed transesterification. Applied Energy 87:1083-1095
Vyas, A.P., Verma, J.L. and Subrahmanyam, N. 2010. A review on FAME production processes. Fuel 89:1-9
Zabeti, M., Daud, W.M.A.W. and Aroua, M.K. 2009. Activity of solid catalysts for biodiesel production: A review. Fuel Processing Technology 90:770–777
Zhang, S., 2010. Rapid microwave-assisted transesterification of yellow horn oil to biodiesel using a heteropolyacid solid catalyst. Bioresource Technology 101:931-936

## Slide 20
Thank you